## Slide 1: Active Noise Cancellation Using the LMS and FxLMS algorithms
November 7, 2016
Marko Stamenovic
Recurse Center Lightning Talk
https://github.com/markostam

## Slide 2: Background and Motivation
Let’s start at the beginning

## Slide 3: Background
Active Noise Cancellation (ANC)
Technique which uses destructive interference to cancel unwanted noise signals.
Machine learning algorithms are employed to quickly learn the characteristics of the unwanted signal in near real time.

## Slide 4
Benefits over passive attenuation
Lighter weight and smaller than passive noise attenuation.
Targets specific frequencies.
Actively adapts to offending noise spectrum.

## Slide 5
Limitations
Expensive.
Not good with impulsive sounds.
Relatively complex (requires specialized hardware and software).
Requires constant power supply.

## Slide 6: System Overview
Equations & block diagrams ahead

## Slide 7: Conceptual System Overview

## Slide 8: Conceptual System Overview

## Slide 9: LMS for ANC Block Diagram
Unknown plant P(z) is the transfer function b/w engine and passenger in car our outside world and ears in headphones.
As e(n) approaches 0, W(z) becomes equal to P(z)

## Slide 10: LMS for ANC Equations
Least Mean Squares (LMS) algorithm. Uses stochastic gradient descent to minimize e(n). Simple and powerful.
= Learning rate

## Slide 11: LMS for ANC Block Diagram and Equations
error e(n)

## Slide 12: Cool story, show me dez code
yn=0.0;
x[0] = refnoise;
for (i = 0; i < N; i++) // compute adaptive filter output (w'x)
{
yn += (weights[i] * x[i]);
}
error = - yn; // compute error
for (i = N-1; i >= 0; i--) // update weights and delay line
{
weights[i] = weights[i] + mu*error*x[i];
x[i] = x[i-1];
}
codec_data.channel[LEFT]= ((uint16_t)(error));
codec_data.channel[RIGHT]= ((uint16_t)(error));
output_sample(codec_data.uint);
return;
}
interrupt void interrupt4(void)
{
short i;
float input, refnoise, signal, signoise, wn, yn, error;
codec_data.uint = input_sample();
refnoise =(codec_data.channel[LEFT]); // noise sensor
input = refnoise;
for (i=0; i < N; i++)
// filter refnoise to emulate transfer
// function of firewall (3rd order lp filter)
{
wn = input - a[i][1]*w[i][0] - a[i][2]*w[i][1];
yn = b[i][0]*wn + b[i][1]*w[i][0] + b[i][2]*w[i][1];
w[i][1] = w[i][0];
w[i][0] = wn;
input = yn;
}

## Slide 13: FxLMS Block Diagram
One thing missing from the LMS model in practical ANC applications is the path from the speakers to the ear for the correction signal.
This is called the Secondary Path or S(z).
The FxLMS or Filtered LMS algorithm takes care of the secondary path.

## Slide 14: FxLMS Block Diagram
By adding in a filter Ŝ(z) equal to S(z), we can account for the secondary path signal.
Ŝ(z) is learned by playing a known excitation signal through the LMS block diagram shown previously.

## Slide 15: FxLMS Block Diagram

## Slide 16: Experimental Results
4

## Slide 17: Experimental Setup
Unknown plant P(z) is modeled by a digital LPF.
Input x(n) is pink noise.
Stays in digital domain so there is no secondary path.

## Slide 18: Learning Rate Too Small
µ = 0.002

## Slide 19: Learning Rate Too Large
µ = 2.6

## Slide 20: Learning Rate Juust Right
µ = 1.3

## Slide 21: Demo Time!!!!!!!!!!!!!!!!!!!!!!
5

## Slide 22: Yes, it’s really time for the:
Long learning rate
Fast learning rate

## Slide 23: Output Waveform
Not Perfect Attenuation
But a lot better than a full
pink noise waveform.

## Slide 24: Thanks!
Any questions ?
Find me at:
markostam@gmail.com
Find my code at:
https://github.com/markostam/active-noise-cancellation